PIEAS TENDER NOTICE

A public sector organization invites sealed tenders from suppliers or their authorized agents/dealers/sole distributors for the following items on FOR Nilore Islamabad Basis.

| Name of Items | Qty | Case Number | Last Date/Time | Opening Date/Time |
| --- | --- | --- | --- | --- |
| i-Hard Grove Index Machine:- Grind-ability Tester for determination the grind-ability of coal, meets ASTM standard D409-51, D409-90, D-409-91, complete with eight 1 inch ball, grinding unit, automatic revolution counter, control switch, weights, built in gear reduction motor, 1/3 HP/220V/1ph/50 Hz, standard coal samples, one gallon of each, 40, 60, 80, 100 HGI. Make: Gilson or equivalent ii-Electric Oven:- Capacity : 32 Liters, Dimensions (W x H x D) Internal (mm) : (400x320x250), Multi-Function Controller Heater: 1.0 KW, Temp. Ambient: ±5 ºC at 300 ºC, Display: LED, Power Supply: AC 230V,1 N ~,50/60Hz. Make: Grieve or equivalent | 01 01 | Tender No. L-154/18-19 | 02/4/2019 1400 Hrs. | 02/4/2019 1430 Hrs. |

- Sealed tenders must be reached to the office of undersigned up to April 02, 2019 at 1400 hrs. and open on the same day at 1430 hrs.

- The envelopes shall be marked as “Tender Number” and “Date of Opening” in bold and legible letters to avoid confusion.

- The quotation must be valid for 90 days.

- The bid found to be the lowest evaluated shall be accepted.

- Firm shall certify that equipment supplied is brand new and strictly according to schedule of the supply order which has been invoiced the onus for any deviation will be the responsibility of the supplier.

- In case the stores found substandard and not according to the specifications as per ordered, the same will have to be rejected and replaced by the supplier at his own cost.

- Liquidated damages may be imposed in the range of 0.5 to 2% per day (on case to case basis depending upon urgency of requirement) and maximum up to 10% of the contract value. In case, the supplier fails to meet the contractual obligation, the purchase will be made at their RISK AND COST.

- Payment will be made after inspection & whole satisfaction of end user.

- 02 % earnest money must be enclosed in shape of CDR/BC/DD/PO in the name PIEAS

- PIEAS has the right to accept/reject the bids without assigning the reasons.

Incharge Procurement

PIEAS, P.O. Nilore, Islamabad

Direct Ph.:-051-9248742, Fax:-051-9248750

PIEAS:- 9248611-20 Ext 3026/3027

E-mail: junaid@pieas.edu.pk

moazzam.ali@pieas.edu.pk